PCHIP Interpolation
CAP-418 Numerical Methods I
2023-05-09

---
Contents
- Objectives
- Gauss-Hermite quadrature method (GHQ)
- Shape-preserving piecewise cubic interpolation (PCHIP)
- Burgers' equation toy problem
- 1D Burgers solution using GHQ
- Comparison of PCHIP and GHQ curves
- Conclusion
- Future works (GPA, 2D Burgers, PINN)

---
Objectives
- Discretization and resampling of functions by bootstrap: PCHIP method
- Application of the PCHIP method to simulate the 1D Burgers equation
- Compare with Gauss-Hermite Quadrature method (GHQ)
- A second phase of the project (work in progress) foresees the use of GPA, 2D Burgers, and PINN

---
Gauss-Hermite Quadrature rule (GHQ)
- A Gaussian quadrature form for approximating integral values
- The solution of the Burgers equation use estimated values calculated using GHQ, as described in the Basdevant et al. (1986) article Spectral and finite difference solutions of the Burgers equation
- The implementation is based on that of John Burkardt https://people.sc.fsu.edu/~jburkardt/

---
Shape-preserving piecewise cubic interpolation (PCHIP)
- PCHIP takes the same form as the GHQ, but with the first derivatives defined in a special way
- The new function values do not exceed the function values at the end of each range
PCHIP
Spline

---
Burgers’ equation toy problem
- Is a fundamental partial differential equation and convection–diffusion equation
- GHQ uses Burgers to generate
  a dataset
- This dataset is then used in
  PCHIP
I.C.
B.C.
Viscosity

---
GHQ implementation
While some algorithms are available, this work has not focused on GHQ

---
GHQ implementation
- The implementation is adapted from the work of J. Burkardt
- Uses an algorithm by Elhay and Kautsky
- The abscissas are the zeros of the N-th order Hermite polynomial
- The integral and the quadrature rule are given by

---
GHQ implementation
Implementation uses Python and Jupyter Notebook
A part of the code is shown below:

---
Parameters

---
Result

---
PCHIP interpolation
- Uses SciPy and the small dataset generated by GHQ
- The points specified in xq (query points) are the x-coordinates for the interpolated function values yq computed by pchip :

---
Result
Using a small dataset of 10 points

---
1D Burgers solution using GHQ
Generates a dataset containing 100 points

---
Only CHG

---
Comparison of PCHIP and GHQ curves

---
Conclusion
- This work compared the PCHIP interpolation method with the Gaussian quadrature method, using the solution of the 1D Burgers equation as a toy problem
- The Gauss-Hermite quadrature method was used both to generate the points that were interpolated and to generate the solution that is compared with PCHIP
- The result shows that there is a certain special deviation near the sharp edges of curves at local maxima or minima. However, the PCHIP method generally showed good performance to interpolate the selected toy problem

---
Future works
- PCHIP implementation using the algorithm (not the library)
- 2D Burgers
  - Rewrite the work
- Gradient Pattern Analysis (GPA)
  - https://github.com/rsautter/GPA (Rubens Sautter)
- PINN (work in progress, see next slide)
- Compare the performances

---
PINN (work in progress)
https://github.com/efurlanm/418/blob/master/burgers-tf-02.ipynb
Burgers
CHG
PINN
TensorFlow v2
Running on GPU
CGH
PINN

---
Thanks
https://github.com/efurlanm/418